## Slide 1
Department of Computer Engineering
Prof. Kishan Makadiya
Computer Organization and Architecture
01CE1402
Unit-3 Programming the Basic Computer

## Slide 2: Outline
Introduction
Machine Language
Assembly Language
Assembler
Program loops
Programming Arithmetic and Logic operations
Subroutines
I-O Programming

## Slide 3: Introduction
  Symbol Hexa code Description
  AND 0 or 8 AND M to AC
  ADD 1 or 9 Add M to AC, carry to E
  LDA 2 or A Load AC from M
  STA 3 or B Store AC in M
  BUN 4 or C Branch unconditionally to m
  BSA 5 or D Save return address in m and branch to m+1
  ISZ 6 or E Increment M and skip if zero
  CLA 7800 Clear AC
  CLE 7400 Clear E
  CMA 7200 Complement AC
  CME 7100 Complement E
  CIR 7080 Circulate right E and AC
  CIL 7040 Circulate left E and AC
  INC 7020 Increment AC, carry to E
  SPA 7010 Skip if AC is positive
  SNA 7008 Skip if AC is negative
  SZA 7004 Skip if AC is zero
  SZE 7002 Skip if E is zero
  HLT 7001 Halt computer
  INP F800 Input information and clear flag
  OUT F400 Output information and clear flag
  SKI F200 Skip if input flag is on
  SKO F100 Skip if output flag is on
  ION F080 Turn interrupt on
  IOF F040 Turn interrupt off

## Slide 4: Machine Language
Program list of instructions or statements for directing the computer to perform a required data processing task.
Various types of programming languages
Binary code
Octal or hexadecimal code
Symbolic code
Each symbolic instruction can be translated into one binary coded instruction. This translation is done by a special program called an Assembler.
High-level Programming language
The Program that translates a high level language program to binary is called a compiler.

## Slide 5: Categories of programs
Binary code
  This is a sequence of instructions and operands in binary that list the exact representation of instructions as they appear in computer memory.
  Example:-
Location | Instruction Code |  |  | 
0 | 0010 | 0000 | 0000 | 0100
1 | 0001 | 0000 | 0000 | 0101
10 | 0011 | 0000 | 0000 | 0110
11 | 0111 | 0000 | 0000 | 0001
100 | 0000 | 0000 | 0101 | 0011
101 | 1111 | 1111 | 1110 | 1001
110 | 0000 | 0000 | 0000 | 0000

## Slide 6: Categories of programs
Octal or hexadecimal code
This is an equivalent translation of the binary code to octal or hexadecimal representation.
Example:-
Location | Instruction
000 | 2004
001 | 1005
002 | 3006
003 | 7001
004 | 0053
005 | FFE9
006 | 0000

## Slide 7: Categories of programs
Symbolic code
  The user employs symbols (letters, numerals, or special characters) for the operation part, the address part, and other parts of the instruction code.
  Each symbolic instruction can be translated into one binary coded instruction by a special program called an assembler and language is referred to as an assembly language program.
Location | Instruction | Comment
000 | LDA 004 | Load first operand into AC
001 | ADD 005 | Add second operand to AC
002 | STA 006 | Store sum in location 006
003 | HLT | Halt computer
004 | 0053 | First operand
005 | FFE9 | Second operand (negative)
006 | 0000 | Store sum here

## Slide 8: Categories of programs
High-level programming languages
  These are special languages developed to reflect the procedures used in the solution of a problem rather than be concerned with the computer hardware behavior. E.g. Fortran, C++, Java, etc.
  The program is written in a sequence of statements in a form that people prefer to think in when solving a problem.
  However, each statement must be translated into a sequence of binary instructions before the program can be executed in a computer.
INTEGER A, B, C
DATA A, 83 B,-23
C = A + B
END

## Slide 9: Assembly Language
Rules of the Language
Each line of an assembly language program is arranged in three columns called fields. The fields specify the following information.
The Label field may be empty or it may specify a symbolic address.
The Instruction field specifies a machine instruction or a pseudo-instruction.
The Comment field may be empty or it may include a comment.

## Slide 10: Rules of the language
A Symbolic Address (in LABEL FIELD) consists of one, two or three, but not more than three alphanumeric characters.
  The first character must be a latter.
  Next two may be latter or numerals.
  The symbolic address is terminated by a comma so that it will be recognized by the assembler.

## Slide 11: Rules of the language
The INSTRUCTION FIELD in program may specify one of the following items:
  A MRI (Memory Reference Instruction)
  A non-MRI (Register Ref. or I/O instructions)
  A pseudo instruction with or without operand.
A MRI occupies two or three symbols separate by space.
Example:
CLA /non MRI
ADD OPR /direct-address MRI
ADD PTR I /Indirect-address MRI

## Slide 12: Rules of the language
The third field in the program is reserved for comments.
It must be preceded by a slash (i.e. to recognize the beginning of a comment)

## Slide 13: Assembly Language
A pseudo instruction is not a machine instruction but rather an instruction to the assembler giving information about some phase of the translation.
Symbol | Information for the Assembler
ORG N | Hexadecimal number N is the memory location for the instruction or operand listed in the following line.
END | Denotes the end of symbolic program.
DEC N | Signed decimal number N to be converted to binary.
HEX N | Hexadecimal number N to be converted to binary

## Slide 14: Assembly Language Program (A.L.P.) to add 2 numbers
Assembly Programming Languages
ORG 0 /Origin of program is location 0
LDA A /Load operand from location A
ADD B /Add operand from location B
STA C /Store sum in location C
HLT /Halt computer
A, DEC 83 /Decimal operand
B, DEC 23 /Decimal operand
C, DEC 0 /Sum stored in location C
END /End of symbolic program

## Slide 15: Assembly Language Program (A.L.P.) to subtract 2 numbers
Label | Instruction | Comment
 | ORG 100 | / Origin of program is location 100
 | LDA B | / Load subtrahend to AC
 | CMA | / Complement AC
 | INC | / Increment AC
 | ADD A | / Add minuend to AC
 | STA C | / Store difference
 | HLT | / Halt computer
A, | DEC 83 | / Minuend
B, | DEC 23 | / Subtrahend
C, | HEX 0 | / Difference stored here
 | END | / End of symbolic program

## Slide 16: Assembly Language Program (A.L.P.) to subtract 2 numbers
Location | Label | Instruction
 |  | ORG 100
100 |  | LDA B
101 |  | CMA
102 |  | INC
103 |  | ADD A
104 |  | STA C
105 |  | HLT
106 | A, | DEC 83
107 | B, | DEC 23
108 | C, | HEX 0
 |  | END
Symbol | Location
A | 106
B | 107
C | 108

## Slide 17: Assembly Language Program (A.L.P.) that evaluates the logic exclusive-OR of two operands
Z = X ⊕ Y = XY’ + X’Y
ORG ---
LDA Y
CMA
AND X
STA TMP
LDA X
CMA
AND Y
ADD TMP
STA Z
HLT
X, ---
Y, ---
Z, ---
TMP, ---
END

## Slide 18: Assembler
An assembler is a program that accepts a symbolic language program and produces its binary machine language equivalent.
The input symbolic program is called the source program and the resulting binary program is called the object program.
The assembler is a program that operates on character strings and produces an equivalent binary interpretation.
To keep track of the location of instructions, the assemble uses a memory word called location counter (LC).

## Slide 19: Hexadecimal Character Code
Character | Code | Character | Code | Character | Code
A | 41 | Q | 51 | 6 | 36
B | 42 | R | 52 | 7 | 37
C | 45 | S | 53 | 8 | 38
D | 44 | T | 54 | 9 | 39
E | 45 | U | 55 | Space | 20
F | 46 | V | 56 | ( | 28
G | 47 | W | 57 | ) | 29
H | 48 | X | 58 | * | 2A
I | 49 | Y | 59 | + | 2B
J | 4A | Z | 5A | , | 2C
K | 4B | 0 | 30 | - | 2D
L | 4C | 1 | 31 | . | 2E
M | 4D | 2 | 32 | / | 2F
N | 4E | 3 | 33 | = | 3D
O | 4F | 4 | 34 | CR | 0D
P | 50 | 5 | 35 |  | 

## Slide 20: Line of Code Table
PL3, LDA SUB I
Memory Word | Symbol | Hexadecimal Code | Binary Representation
1 | P L | 50 4C | 0101 0000 0100 1100
2 | 3 , | 33 2C | 0011 0011 0010 1100
3 | L D | 4C 44 | 0100 1100 0100 0100
4 | A | 41 20 | 0100 0001 0010 0000
5 | S U | 53 55 | 0101 0011 0101 0101
6 | B | 42 20 | 0100 0010 0010 0000
7 | I CR | 49 0D | 0100 1001 0000 1101

## Slide 21: First Pass of an assembler
LC ← 0
Scan next line of code
Label
Store address in symbol table together with value of LC
Increment LC
Set LC
ORG
END
Go to second pass
First pass
no
no
no
yes
yes
yes

## Slide 22
LC ← 0
Scan next line of code
Pseudo-instruction
Store binary equivalent of instruction in location given by LC
Increment LC
Set LC
ORG
END
Second pass
Yes
No
No
No
Yes
Yes
Done
Convert operand to binary and store in location given by LC
MRI
No
Valid non-MRI instruction
Get operation code and set bits 2-4
Search address-symbol table for binary equivalent of symbolic address and set bits 5-16
I
Set first bit to 1
Set first bit to 0
Yes
No
Assemble all parts of binary instruction and store in location given by LC
Yes
Error in line of code
No
Yes
DEC or HEX
Second Pass
of an assembler

## Slide 23: Program Loops
A program loop is a sequence of instructions that are executed many times, each time with a different set of data.
A system program that translates a program written in a high-level programming language to a machine language program is called a compiler.

## Slide 24
ORG 100
/Origin of program is HEX 100
LDA ADS
/Load first address of operands
STA PTR
/Store in pointer
LDA NBR
/Load minus 100
STA CTR
/Store in counter
LOP,
CLA
/Clear accumulator
ADD PTR I
/Add an operand to AC
ISZ PTR
/Increment pointer
ISZ CTR
/Increment counter
BUN LOP
/Repeat loop again
STA SUM
/Store sum
HLT
/Halt
ADS,
HEX 150
/First address of operands
PTR,
HEX 0
/This location reserved for pointer
NBR,
DEC -100
/Constant to initialized counter
CTR,
HEX 0
/This location reserved for a counter
SUM,
HEX 0
/Sum is store here
ORG 150
/Origin of operands is HEX 150
DEC 75
/First operand
DEC 23
/Last operand
END
/End of symbolic program
.
.
Assembly Language Program to add 100 numbers

## Slide 25: Assembly Language Program (A.L.P.) to clear the contents of hex locations 500 to 5FF with 0
ORG 100
/Origin of program is HEX 100
LDA ADS
/Load first address of operands
STA PTR
/Store in pointer
LDA NBR
/Load minus 255
STA CTR
/Store in counter
LOP,
CLA
/Clear accumulator
STA PTR I
/Store zero to location pointed by PTR
ISZ PTR
/Increment pointer
ISZ CTR
/Increment counter
BUN LOP
/Repeat loop again
HLT
/Halt
ADS,
HEX 500
/First address of operands
PTR,
HEX 0
/This location reserved for pointer
NBR,
DEC -255
/Constant to initialized counter
CTR,
HEX 0
/This location reserved for a counter
END
/End of symbolic program

## Slide 26: Programming Arithmetic & logic Operations
Multiplication Program
Multiplying two numbers
For simplify, neglect the sign bit and assume positive numbers
Assume that two binary numbers have no more than eight significant bits so their product can not exceed the word capacity of 16 bits.
It is possible to modify to take care of signs or use 16-bit numbers.
Adding the multiplicand X as many times as there are 1’s in multiplier Y, provided that the value of X is shifted left from one line to the next.
Since, the computer can add only two numbers at a time, we reserve a memory location P, to store intermediate sums (called partial product).

## Slide 27: Programming Arithmetic & logic Operations
X holds the multiplicand
Y holds the multiplier
P holds the product
Example with four
significant digits
X = 1111 P
Y = 1011 0000 0000
1111 0000 1111
1 1110 0010 1101
00 0000 0010 1101
111 1000 1010 0101
1010 0101
cil
CTR  - 8
P  0
E  0
AC  Y
Y  AC
cir EAC
E
P  P + X
E  0
AC  X
cil EAC
X  AC
CTR  CTR + 1
=1
=0
CTR
=0
Stop
 0

## Slide 28
ORG 100
CLE
LDA Y
CIR
STA Y
SZE
BUN ONE
BUN ZRO
LDA X
ADD P
STA P
CLE
LDA X
CIL
STA X
ISZ CTR
BUN LOP
HLT
DEC -8
HEX 000F
HEX 000B
HEX 0
END
/ Clear E
/ Load multiplier
/ Transfer multiplier bit to E
/ Store shifted multiplier
/ Check if bit is zero
/ Bit is one; goto ONE
/ Bit is zero; goto ZRO
/ Load multiplicand
/ Add to partial product
/ Store partial product
/ Clear E
/ Load multiplicand
/ Shift left
/ Store shifted multiplicand
/ Increment counter
/ Counter not zero; repeat loop
/ Counter is zero; halt
/ This location serves as a counter
/ Multiplicand stored here
/ Multiplier stored here
/ Product formed here
LOP,
ONE,
ZRO,
CTR,
X,
Y,
P,
cil
CTR  - 8
P  0
E  0
AC  Y
Y  AC
cir EAC
E
P  P + X
E  0
AC  X
cil EAC
X  AC
CTR  CTR + 1
=1
=0
CTR
=0
Stop
 0

## Slide 29: Programming Arithmetic & logic Operations
Double-Precision Addition
When two 16-bit unsigned numbers are multiplied, the result is a 32-bit product that must be stored in two memory words.
A number stored in two memory words is said to have double precision.
When a partial product is computed, it is necessary that a double precision number be added to the shifted multiplicand, which is also a double precision number.

## Slide 30: Assembly Language Program (A.L.P.) to Add Two Double-Precision Numbers
ORG 100
/Origin of program is HEX 100
LDA AL
/Load A low
ADD BL
/Add B low, carry in E
STA CL
/Store in C low
CLA
/Clear AC
CIL
/Circulate to bring carry into AC(16)
ADD AH
/Add A high and carry
ADD BH
/Add B high
STA CH
/Store in C high
HLT
/Halt
AL, -
AH, -
BL, -
BH, -
CL, -
CH, -

## Slide 31: Logic and Shift Operations
Logic Operations
The basic computer has three machine instructions that perform logic operations: AND, CMA and CLA
The LDA instruction may be considered as a logic operation that transfers a logic operand into the AC.
We know 16 different logic operations. All 16 operations can be implemented using AND and Complement operations.
Program for OR operation - x + y = (x’ y’)’
  ORG 100
  LDA X / Load 1st operand X
  CMA / Complement to get X’
  STA TMP / Store in a temporary location
  LDA Y / Load 2nd operand Y
  CMA / Complement to get Y’
  AND TMP / AND with X’ to get X’ AND Y’
  CMA / Complement again to get X OR Y
  X, -
  Y, -
  TMP, -
  END

## Slide 32: Logic and Shift Operations
Shift Operations
The basic computer has circular-shift operations as machine instructions.
The other shifts of interest are the logical shifts and arithmetic shifts, which can be programmed with a small number of instructions.
Logical shift-right // zero be added to left most position
  CLE
  CIR
Logical shift-left //zero be added to right most position
  CLE
  CIL

## Slide 33: Logic and Shift Operations
Shift Operations (Cont..)
Arithmetic right-shift
  CLE / Clear E to 0
  SPA / Skip if AC is positive
  CME / AC is negative; set E to 1
  CIR / Circulate E and AC
Arithmetic left-shift
  Added bit in the least significant position be 0.
  CLE / Clear E to 0
  CIL / Circulate E and AC
  The sign bit must not change during the shift.
  After shifting, compare E and AC(15)
  If equal, correct shift
  If not equal, an overflow occurs.

## Slide 34: Subroutines
The procedure for branching to a subroutine and returning to the main program is referred to as a subroutine linkage.
The BSA instruction performs an operation commonly called subroutine call.
The last instruction of the subroutine performs an operation commonly called subroutine return.
Subroutine Parameters and Data Linkage
Transferred two operands to the subroutine and subroutine return the result of the operation
AC can be used to transfer one operand and to receive the result. The other operand is inserted in the location following the BSA instruction.

## Slide 35: Subroutines
A set of common instructions that can be used in a program many times is called a subroutine.
Each time that a subroutine is used in the main part of the program, a branch is executed to the beginning of the subroutine.
After the subroutine has been executed, a branch is made back to the main program.
A subroutine consists of a self contained sequence of instructions that carries a given task.
ORG 100
100
LDA X
101
BSA SH4
102
STA X
103
LDA Y
104
BSA SH4
105
STA Y
106
HLT
107
HEX 1234
X,
108
HEX 4321
Y,
109
HEX 0
10A
CIL
10B
CIL
10C
CIL
10D
CIL
10E
AND MSK
10F
BUN SH4 I
110
HEX FFF0
MSK,
END
SH4,

## Slide 36: Example: Subroutine performing LOGICAL OR operation; Need two parameters
ORG 200
LDA X / Load 1st operand into AC
BSA OR / Branch to subroutine OR
HEX 3AF6 / 2nd operand stored here
STA Z / Subroutine returns here
HLT
X, HEX 7B95 / 1st operand stored here
Z, HEX 0 / Result stored here
OR, HEX 0 / Subroutine OR
CMA / Complement 1st operand
STA TMP / Store in temporary location
LDA OR I / Load 2nd operand
CMA / Complement 2nd operand
AND TMP / AND complemented 1st operand
CMA / Complement again to get OR
ISZ OR / Increment return address
BUN OR I / Return to main program
TMP, HEX 0 / Temporary storage
END

## Slide 37: I-O Programming - A.L.P. to input one character
1
ORG 100
/Origin of program is HEX 100
2
SKI
/Check input flag
3
BUN CIF
4
INP
/Flag = 1, input character
5
OUT
/Print character
6
CHR,
STA CHR
/Store character
7
HLT
8
-
/Store character here
9
END
CIF,

## Slide 38: I-O Programming - A.L.P. to output one character
1
ORG 100
/Origin of program is HEX 100
2
LDA CHR
/Load character into AC
3
SKO
/Check output flag
4
BUN COF
5
OUT
/Flag = 1, output character
CHR,
6
HLT
7
HEX 0057
/Character is “W”
8
END
COF,

## Slide 39: Thank You !!!