## Slide 1: Unit-4 Microprogrammed Control
krunal.vyas@darshan.ac.in
9601901005
Computer Engineering Department
Prof. Krunal D. Vyas
Computer Organization & Architecture (COA)
GTU # 3140707

## Slide 2

Looping
Outline
  Control Memory
  Address Sequencing
  Microinstruction Code Format
  Questions asked in GTU exam

## Slide 3: Control Memory
Section - 1

## Slide 4: Microprogrammed Control Organization
Next-address generator (Sequencer)
Control address register
Control memory
(ROM)
Control
data
register
Next-address information
Control
word
External
input

## Slide 5: Control Memory
A computer that employs a microprogrammed control unit will have two separate memories: a main memory and a control memory.
The control memory holds a fixed microprogram that can not be altered by the occasional user.
The microprogram consists of microinstructions that specify various internal control signals for execution of register microoperation.
Microinstructions generates the microoperations to fetch instruction from main memory; to evaluate the effective address, to execute the operation specified by the instruction, and to return control to the fetch of next instruction.

## Slide 6: Address Sequencing
Section - 2

## Slide 7: Address Sequencing
Microinstructions are stored in control memory in groups, with each group specifying a routine.
The transformation from the instruction code bits to an address in control memory where the routine is located is referred to as a mapping process.
The address sequencing capabilities required in a control memory are:
  Incrementing of the control address register.
  Unconditional branch or conditional branch, depending on status bit conditions.
  A mapping process from the bits of the instruction to an address for control memory.
  A facility for subroutine call and return.

## Slide 8: Address Sequencing
Instruction code
Mapping
logic
Multiplexer
Control address register
(CAR)
Control memory
Branch
logic
Subroutine
register
(SBR)
Incrementer
Mux
select
Status
bits
Clock
Select a status bit
Branch address
Microoperations

## Slide 9: Microinstruction Code Format
Section - 3

## Slide 10: Microinstruction Code Format
F1
F2
F3
CD
BR
AD
3
3
3
2
2
7
F1, F2, F3: Microoperation fields
CD: Condition for branching
BR: Branch field
AD: Address field

## Slide 11: Symbols & Binary Code for Microinstruction Fields
F1 | Microoperation | Symbol
000 | None | NOP
001 | AC AC + DR | ADD
010 | AC 0 | CLRAC
011 | AC AC + 1 | INCAC
100 | AC DR | DRTAC
101 | AR DR(0-10) | DRTAR
110 | AR PC | PCTAR
111 | M[AR] DR | WRITE
F2 | Microoperation | Symbol
000 | None | NOP
001 | AC AC - DR | SUB
010 | AC AC DR | OR
011 | AC AC DR | AND
100 | DR M[AR] | READ
101 | DR AC | ACTDR
110 | DR DR + 1 | INCDR
111 | DR(0-10) PC | PCTDR

## Slide 12: Symbols & Binary Code for Microinstruction Fields
F3 | Microoperation | Symbol
000 | None | NOP
001 | AC AC + DR | XOR
010 | AC AC’ | COM
011 | AC shl AC | SHL
100 | AC shr AC | SHR
101 | PC PC + 1 | INCPC
110 | PC AR | ARTPC
111 | Reserved | 
CD | Symbol | Comments
00 | U - 1 | Unconditional branch
01 | I - DR(15) | Indirect address bit
10 | S - AC(15) | Sign bit of AC
11 | Z - AC = 0 | Zero value in AC
BR | Symbol | Function
00 | JMP | CAR AD if condition = 1, CAR CAR+1 if condition = 0
01 | CALL | CAR AD, SBR CAR+1 if condition=1, CAR CAR+1 if condition=0
10 | RET | CAR SBR (Return from subroutine)
11 | MAP | CAR(2-5) DR(11-14), CAR(0,1,6) 0

## Slide 13: Questions asked in GTU exam
Section - 4

## Slide 14: Questions asked in GTU exam
Draw and explain flow chart of address sequencing.
Draw and explain 20 bits microinstruction code format.
What is micro-programmed control architecture?
Explain Control Memory.